Address / (HEX)	Register Operation / Write Read
$D1E0	Set address A15-A8 for $D600 RAM window. (LSB of sector number.) Set RST- signal true (low). Resets the / SCSI/SASI bus. (RST- also true during RESET)
$D1E1	Set printer data and SCSI/SASI data. True logic for printer — Inverted for SCSI/SASI bus. Read data from SCSI/SASI bus. Data is inverted.
$D1E2	General purpose outputs. / B[3..0] High RAM address, / sets address A19-A16. / B[4] 1 = Set SEL- true / B[5] 1 = Enable RAM access / B[6] 1 = Set STROBE- true / B[7] 1 = Enable Parallel IRQ General purpose inputs. / B[0] = SASI C/D- / B[1] = SASI MSG- / B[2] = SASI I/O- / B[4] = Printer FAULT- / B[5] = SASI BUSY- / B[6] = Printer BUSY / B[7] = SASI REQ- / Also clears RST- signal
$D1E3 / or / $D1FF	Set ROM enable and bank. Only / 1 bit allowed set at a time. / B[2] 1 = Disk Interface ROM / B[3] 1 = Seg 2 of setup MENU / B[4] 1 = R:/P: Handler ROM / B[5] 1 = Seg 1 of setup MENU / B[7..6] High RAM address, set address A21-A20 / All bits 0 disable the ROM. IRQ sense bits + Misc inputs. / B[0] = RS-232 DCD line / B[1] = RS-232 DSR line / B[2] = RS-232 CTS line / B[3] = Printer BUSY- IRQ / B[4] = MIO IRQ (from 6551 or / Printer BUSY- IRQ)
$D1C0	Write ACIA transmit register. Read ACIA receive register.
$D1C1	Perform a programmed RESET on ACIA (data is "don't care"). Read Status register (resets IRQ). / B[0] 1 = Parity error / B[1] 1 = Framing error / B[2] 1 = Overrun has occurred / B[3] 1 = Receiver reg. full / B[4] 1 = Transmitter empty / B[7] 1 = IRQ occurred
$D1C2	Write ACIA command register. Read ACIA command register.
$D1C3	Write ACIA control register. Read ACIA control register.
$D6xx	Write RAM. High address A21-A8 selected / by $D1E0/$D1E2/$D1E3 Read RAM. High address A21-A8 / selected by $D1E0/D1E2/$D1E3.

Addressing the RAM

The MIO standard board can access up to 1 Megabyte of RAM which takes 20 bits to address. Address bits A19-A16 are set from writing to the latch at $D1E2, bits A15-A8 are set from writing to the latch at
$D1E0, and bits A7-A0 are CPU address lines A7-A0 when reading/writing $D6xx. Thus there are up
to 4096 "pages" of memory that may appear at the $D6xx window.
The DUO MIO board add two extra bits for addressing up to 4 Megabyte of RAM which takes 22 bits to address (A20-A21). Those extra bits are at $D1E3 or $D1FF, bits 6/7.
In order to access the memory, it must first be enabled by setting $D1E2 bit 5 to "1" (this also turns
on the MIO's red LED and the DUO MIO’s amber LED). It is generally a good idea to leave the RAM disabled while not using it in
case of a system crash (which could inadvertently write in the $D6xx window).